SSH Tunnels - Requirements
PROBLEM
Pi sited at observatory, behind a firewall with outgoing access only, the controlling server is remote and on the internet.
REQUIREMENTS
- The Pi – server need to securely communicate telescope commands via an MQTT service running on the server.
- I need to remotely connect to the Pi for maintenance purposes.

---
Overview
Observatory
pi
Webparametrics.co.uk
Internet
MQTT
Internal network
LXC containers

---
MQTT – using LOCAL TUNNEL
webparametrics.co.uk has the mqtt service listening on 10.105.192.1, port 1883, this address is on an internal network of the server. The mqtt service is not visible to the internet.
On the pi, this command is run:
ssh -L 1883:10.105.192.1:1883 bernard@webparametrics.co.uk
The mqtt client on the pi talks to localhost:1883, expecting an mqtt server to be listening there.
This is forwarded to webparametrics.co.uk, where it connects to 10.105.192.1:1883, and hence the mqtt client connects to the mqtt service.

---
Local Tunnel
Pi
Internet
Localhost
Webparametrics.co.uk
MQTT Client
MQTT
10.105.192.1
MQTT Client calls localhost :1883
This is tunnelled to 10.105.192.1:1883
On webparametrics.co.uk
Containers

---
MQTT – using LOCAL TUNNEL
The full command used is:
ssh -NT -o ServerAliveInterval=60 -o ExitOnForwardFailure=yes -L 1883:10.105.192.1:1883 bernard@webparametrics.co.uk
The above is all on a single line, with options:
-N Do not execute a remote command.
-T Disable pseudo-terminal allocation.
-o Apply option normally set in a configuration file.
-NT stops a remote terminal being created, and a bash shell from running, which is the normal operation when an ssh call is made. But we just want the tunnel.

---
Access – using REMOTE TUNNEL
Aim – allow a user on webparametrics.co.uk to open a connection to the pi, despite it being behind a firewall.
On the pi, this command is run (choose any free port, in this case 8888), which creates a ‘remote’ tunnel.
ssh -R 8888:localhost:22 bernard@webparametrics.co.uk
If this tunnel exists, then a user on webparametrics.co.uk can connect to localhost:8888, and the connection will be forwarded to the pi localhost:22
So on the server webparametrics.co.uk I can call:
ssh -p 8888 localhost

---
Remote Tunnel
Pi
Internet
Webparametrics.co.uk
Localhost
SSH Server
Localhost
USER
User on webparametrics calls localhost:8888 (using ssh -p 8888 localhost)
This is tunnelled to localhost:22 on the pi

---
Access – using REMOTE TUNNEL
The full command to create the tunnel is:
ssh -NT -o ServerAliveInterval=60 -o ExitOnForwardFailure=yes -R 8888:localhost:22 bernard@webparametrics.co.uk
In both cases, the tunnels are created from the pi, in the outgoing direction (so allowed through the firewall).
The tunnels need to be up permanently, and restart automatically if down.
Next step: create two services on the pi, which start the tunnels on boot up.

---
mqtttunnel.service
[Unit]
Description=Tunnel to mqtt server
After=network.target
[Service]
User=bernard
Restart=on-failure
RestartSec=5
ExecStart=/usr/bin/ssh -NT -o ServerAliveInterval=60 -o ExitOnForwardFailure=yes -L 1883:10.105.192.1:1883 bernard@webparametrics.co.uk
StandardOutput=null
StandardError=journal
[Install]
WantedBy=multi-user.target

---
remotaccess.service
[Unit]
Description=Tunnel to webparametrics allowing remote access
After=network.target
[Service]
User=bernard
Restart=on-failure
RestartSec=5
ExecStart=/usr/bin/ssh -NT -o ServerAliveInterval=60 -o ExitOnForwardFailure=yes -R 8888:localhost:22 bernard@webparametrics.co.uk
StandardOutput=null
StandardError=journal
[Install]
WantedBy=multi-user.target

---
Notes:
Passwords are not useable in this automated tunnel creation process, so keys must be used.
User=bernard ensures bernard’s public/private keys are used to create the tunnels.
ServerAliveInterval keeps a signal going, even if no traffic present, this keeps the router address translation working.
ExitOnForwardFailure ensures the command exits on failure with a failed exit code, allowing the systemd service to restart the ssh tunnel.

---
Enable services on the pi
As root, set mqtttunnel.service into the system directory as:
/lib/systemd/system/mqtttunnel.service
Enable the service with the following commands:
systemctl daemon-reload
systemctl enable mqtttunnel.service
systemctl start mqtttunnel
Do the same with remoteaccess.service, and the tunnels will start on boot up and be permanently maintained.

---
Moving MQTT server
I later decided the MQTT server was better sited on the pi. This requires a remote tunnel rather than local, however it needs to terminate on an ip address to allow the LXC containers access.
Observatory
Webparametrics.co.uk
10.105.192.1
Pi
MQTT
Internet
LXC containers

---
Remote Gateway Tunnel
The MQTT server is now running on the pi as localhost:1883.
The webparametrics server should serve this on 10.105.192.1:1883
This needs the following tunnel setting up:
ssh -R 10.105.192.1:1883:localhost:1883 bernard@webparametrics.co.uk
As default the SSH Tunnel only allows local connection, but in this instance the LXC containers need access to the MQTT service by calling 10.105.192.1 so webparametrics is acting as a gateway.
To enable this the webparametrics server needs an extra setting in etc/ssh/sshd_config, the line:
GatewayPorts clientspecified
The ‘clientspecified’ keyword indicates the listening ip is specified in the tunnel setup command as shown above.

---
Remote Tunnel and Gateway
Pi
Internet
Webparametrics.co.uk
Localhost
MQTT Server
10.105.192.1
MQTT client programs on the LXC containers call 10.105.192.1:1883 which is forwarded to localhost:1883 on the pi.